/*ROBS 16 PAD KIT...16 PADS IN CHRONOLOGICAL ORDER.

* //TEMPLATE FOR EZDRUMMER 'METAL HEADS'KIT

*/

//Piezo defines

#define NUM_PIEZOS 16

#define PAD1_THRESHOLD 10

#define PAD2_THRESHOLD 10

#define PAD3_THRESHOLD 10

#define PAD4_THRESHOLD 10

#define PAD5_THRESHOLD 10     //MIN/MAX VELOCITIES/sensitivity...

#define PAD6_THRESHOLD 10

#define PAD7_THRESHOLD 10

#define PAD8_THRESHOLD 10

#define PAD9_THRESHOLD 10

#define PAD10_THRESHOLD 10

#define PAD11_THRESHOLD 10

#define PAD12_THRESHOLD 10

#define PAD13_THRESHOLD 10

#define PAD14_THRESHOLD 10

#define PAD15_THRESHOLD 10

#define PAD16_THRESHOLD 10

#define START_SLOT 0     //0 START ANALOG INPUTS

//MIDI note defines for each trigger

#define PAD1_NOTE 34  //pad1 kick  +

#define PAD2_NOTE 38  //pad2 snare +

#define PAD3_NOTE 22  //pad3 closed hat +)) to be switched 22

#define PAD4_NOTE 17  //pad4 open hat +  )) 17 to be switched to closed (22)^

#define PAD5_NOTE 53 //pad5 ride bell +

#define PAD6_NOTE 91  //pad6 ride cymbal +      MIDI NOTE NUMBERS..ALL SETUP

#define PAD7_NOTE 32  //pad7 crash 2 +

#define PAD8_NOTE 82  //pad8 hi tom 1 +

#define PAD9_NOTE 80  //pad9 mid tom +

#define PAD10_NOTE 45  //pad10 low tom 3 +

#define PAD11_NOTE 43  //pad11 hi floor tom 1 +

#define PAD12_NOTE 41  //pad12 low floor tom 2 +

#define PAD13_NOTE 49 //pad13 crash cymbal 1 +

#define PAD14_NOTE 57  //pad14 crash cymbal 2 +

#define PAD15_NOTE 55  //pad15 splash 1 +

#define PAD16_NOTE 31  //pad16 splash 3 +

//MIDI defines

#define NOTE_ON_CMD 0x90

#define NOTE_OFF_CMD 0x80

#define MAX_MIDI_VELOCITY 127

//MIDI baud rate

#define SERIAL_RATE 31250

//Program defines

//ALL TIME MEASURED IN MILLISECONDS

#define SIGNAL_BUFFER_SIZE 50

#define PEAK_BUFFER_SIZE 10

#define MAX_TIME_BETWEEN_PEAKS 10

#define MIN_TIME_BETWEEN_NOTES 10

//map that holds the mux slots of the piezos

unsigned short slotMap[NUM_PIEZOS];

//map that holds the respective note to each piezo

unsigned short noteMap[NUM_PIEZOS];

//map that holds the respective threshold to each piezo

unsigned short thresholdMap[NUM_PIEZOS];

//Ring buffers to store analog signal and peaks

short currentSignalIndex[NUM_PIEZOS];

short currentPeakIndex[NUM_PIEZOS];

unsigned short signalBuffer[NUM_PIEZOS][SIGNAL_BUFFER_SIZE];

unsigned short peakBuffer[NUM_PIEZOS][PEAK_BUFFER_SIZE];

boolean noteReady[NUM_PIEZOS];

unsigned short noteReadyVelocity[NUM_PIEZOS];

boolean isLastPeakZeroed[NUM_PIEZOS];

unsigned long lastPeakTime[NUM_PIEZOS];

unsigned long lastNoteTime[NUM_PIEZOS];

//Variables used for switch mod

byte hihat_switch = 0;

unsigned long switch_pressed = 0;

void setup()

{

Serial.begin(SERIAL_RATE);

//initialize globals

for(short i=0; i<NUM_PIEZOS; ++i)

{

currentSignalIndex[i] = 0;

currentPeakIndex[i] = 0;

memset(signalBuffer[i],0,sizeof(signalBuffer[i]));

memset(peakBuffer[i],0,sizeof(peakBuffer[i]));

noteReady[i] = false;

noteReadyVelocity[i] = 0;

isLastPeakZeroed[i] = true;

lastPeakTime[i] = 0;

lastNoteTime[i] = 0;

slotMap[i] = START_SLOT + i;

}

thresholdMap[0] = PAD1_THRESHOLD;

thresholdMap[1] = PAD2_THRESHOLD;

thresholdMap[2] = PAD3_THRESHOLD;

thresholdMap[3] = PAD4_THRESHOLD;

thresholdMap[4] = PAD5_THRESHOLD;

thresholdMap[5] = PAD6_THRESHOLD;

thresholdMap[6] = PAD7_THRESHOLD;

thresholdMap[7] = PAD8_THRESHOLD;

thresholdMap[8] = PAD9_THRESHOLD;

thresholdMap[9] = PAD10_THRESHOLD;

thresholdMap[10] = PAD11_THRESHOLD;

thresholdMap[11] = PAD12_THRESHOLD;

thresholdMap[12] = PAD13_THRESHOLD;

thresholdMap[13] = PAD14_THRESHOLD;

thresholdMap[14] = PAD15_THRESHOLD;

thresholdMap[15] = PAD16_THRESHOLD;

noteMap[0] = PAD1_NOTE;

noteMap[1] = PAD2_NOTE;

noteMap[2] = PAD3_NOTE;

noteMap[3] = PAD4_NOTE;

noteMap[4] = PAD5_NOTE;

noteMap[5] = PAD6_NOTE;

noteMap[6] = PAD7_NOTE;

noteMap[7] = PAD8_NOTE;

noteMap[8] = PAD9_NOTE;

noteMap[9] = PAD10_NOTE;

noteMap[10] = PAD11_NOTE;

noteMap[11] = PAD12_NOTE;

noteMap[12] = PAD13_NOTE;

noteMap[13] = PAD14_NOTE;

noteMap[14] = PAD15_NOTE;

noteMap[15] = PAD16_NOTE;

}

void loop()

{

unsigned long currentTime = millis();

if(currentTime > (switch_pressed + 2))

{

hihat_switch = (((hihat_switch << 1) | digitalRead(3)) & 3);

if(hihat_switch == 2){

noteFire(22, 127);

switch_pressed = currentTime;

}

if(hihat_switch == 1){

noteFire(17, 127);

switch_pressed = currentTime;

}

}

for(short i=0; i<NUM_PIEZOS; ++i)

{

//get a new signal from analog read

unsigned short newSignal = analogRead(slotMap[i]);

signalBuffer[i][currentSignalIndex[i]] = newSignal;

//if new signal is 0

if(newSignal < thresholdMap[i])

{

if(!isLastPeakZeroed[i] && (currentTime - lastPeakTime[i]) > MAX_TIME_BETWEEN_PEAKS)

{

recordNewPeak(i,0);

}

else

{

//get previous signal

short prevSignalIndex = currentSignalIndex[i]-1;

if(prevSignalIndex < 0) prevSignalIndex = SIGNAL_BUFFER_SIZE-1;

unsigned short prevSignal = signalBuffer[i][prevSignalIndex];

unsigned short newPeak = 0;

//find the wave peak if previous signal was not 0 by going

//through previous signal values until another 0 is reached

while(prevSignal >= thresholdMap[i])

{

if(signalBuffer[i][prevSignalIndex] > newPeak)

{

newPeak = signalBuffer[i][prevSignalIndex];

}

//decrement previous signal index, and get previous signal

prevSignalIndex--;

if(prevSignalIndex < 0) prevSignalIndex = SIGNAL_BUFFER_SIZE-1;

prevSignal = signalBuffer[i][prevSignalIndex];

}

if(newPeak > 0)

{

recordNewPeak(i, newPeak);

}

}

}

currentSignalIndex[i]++;

if(currentSignalIndex[i] == SIGNAL_BUFFER_SIZE) currentSignalIndex[i] = 0;

}

}

void recordNewPeak(short slot, short newPeak)

{

isLastPeakZeroed[slot] = (newPeak == 0);

unsigned long currentTime = millis();

lastPeakTime[slot] = currentTime;

//new peak recorded (newPeak)

peakBuffer[slot][currentPeakIndex[slot]] = newPeak;

//1 of 3 cases can happen:

// 1) note ready - if new peak >= previous peak

// 2) note fire - if new peak < previous peak and previous peak was a note ready

// 3) no note - if new peak < previous peak and previous peak was NOT note ready

//get previous peak

short prevPeakIndex = currentPeakIndex[slot]-1;

if(prevPeakIndex < 0) prevPeakIndex = PEAK_BUFFER_SIZE-1;

unsigned short prevPeak = peakBuffer[slot][prevPeakIndex];

if(newPeak > prevPeak && (currentTime - lastNoteTime[slot])>MIN_TIME_BETWEEN_NOTES)

{

noteReady[slot] = true;

if(newPeak > noteReadyVelocity[slot])

noteReadyVelocity[slot] = newPeak;

}

else if(newPeak < prevPeak && noteReady[slot])

{

noteFire(noteMap[slot], noteReadyVelocity[slot]);

noteReady[slot] = false;

noteReadyVelocity[slot] = 0;

lastNoteTime[slot] = currentTime;

}

currentPeakIndex[slot]++;

if(currentPeakIndex[slot] == PEAK_BUFFER_SIZE) currentPeakIndex[slot] = 0;

}

void noteFire(unsigned short note, unsigned short velocity)

{

if(velocity > MAX_MIDI_VELOCITY)

velocity = MAX_MIDI_VELOCITY;

if((note == 17) && (hihat_switch == 0)) //if pad 4 is hit (note 17) and switch is pressed change note to 22

{

note = 22;

}

midiNoteOn(note, velocity);

midiNoteOff(note, velocity);

}

void midiNoteOn(byte note, byte midiVelocity)

{

Serial.write(NOTE_ON_CMD);

Serial.write(note);

Serial.write(midiVelocity);

}

void midiNoteOff(byte note, byte midiVelocity)

{

Serial.write(NOTE_OFF_CMD);

Serial.write(note);

Serial.write(midiVelocity);

}